## Slide 1
WORK INTEGRATED LEARNING / 2026
CONNECTING CARE.
SECURING DATA.
BRIDGING THE DIVIDE.
Jane Furse Memorial Hospital Network Infrastructure Project
Developing a sustainable, secure and reliable connection to the Sekhukhune District Municipality network
TASK 1 + TASK 2 • DIPLOMA IN INFORMATION TECHNOLOGY MANAGEMENT

## Slide 2
WIL PROJECT / JANE FURSE
The project at a glance
A one-year transformation of connectivity, computing, data protection and ICT capability.
01
A dedicated municipal-to-hospital network will provide the foundation for more dependable digital healthcare and connected operations.
Install an approximately 1 km fibre link with mobile failover.
Modernise endpoints, shared printing, servers and storage.
Introduce EHR, integrated finance and supply-chain workflows.
Strengthen security, backup, governance and ICT staff capability.
600
STAFF
Across shifts
100
PATIENTS / DAY
Approximate volume
12
MONTHS
Planned delivery
R8.3–14.5m
BUDGET
Estimated total
OUTCOME: RELIABLE, SECURE DIGITAL CARE

## Slide 3
WIL PROJECT / JANE FURSE
A rural hospital with district-wide importance
Jane Furse Memorial Hospital serves the Sekhukhune District in Limpopo.
02
The network gap is more than a technology issue: it affects how quickly staff can find patient information, communicate with suppliers and keep critical services running.
01 KM
From municipal offices
20
Patient wards
5
Administration offices
3
ICT support personnel
PROJECT CONTEXT
Sekhukhune District
Limpopo, South Africa
The municipality has an existing network. The hospital sits approximately one kilometre away, creating a clear opportunity to extend connectivity.
Carrier constraint
Openserve is the only carrier identified in the project documents.

## Slide 4
WIL PROJECT / JANE FURSE
The current state creates avoidable friction
Outdated devices, disconnected systems and weak data protection slow down daily work.
03
15
OLD COMPUTERS
3
PRINTERS
0
CENTRAL STORAGE
0
FIREWALL / AV BASELINE
PATIENT RECORDS
Paper files go missing; no central searchable database.
FINANCE
Separate systems slow reporting and prevent easy municipal data exchange.
SUPPLY CHAIN
Unreliable connectivity slows Intralink orders and can cause duplicates.
ICT CAPACITY
Three support staff spend too much time fixing old computers.

## Slide 5
WIL PROJECT / JANE FURSE
Why the project needs to happen now
Delays preserve risks to patient safety, data integrity and service continuity.
04
01
Patient safety
Missing or slow-to-find records can delay care and increase the risk of error.
02
Cybersecurity
Without effective controls, patient and financial information is exposed.
03
Staff productivity
Slow machines and manual work reduce time available for core duties.
04
Strategic alignment
Supports digital health direction, POPIA-focused data management and SDGs 3 and 9.
05
Funding window
The municipality has identified the project as a priority for funding.

## Slide 6
WIL PROJECT / JANE FURSE
What success must deliver
Project goals translated into tangible outcomes and acceptance measures.
05
CONNECT
Dedicated fibre link
≤10 ms target latency; 99.9% uptime target
MODERNISE
40+ workstations
At least 40 modern desktop computers
PROTECT
Secure data & network
Firewall, endpoint protection, encryption and access controls
RECOVER
Reliable backup
Automated backups; documented restore tests
INTEGRATE
Connected applications
EHR, finance, Intralinks and municipal workflows
EMPOWER
Build ICT capacity
Three ICT staff trained with SOPs and manuals
DELIVERY WINDOW • SEPTEMBER 2026 — AUGUST 2027

## Slide 7
WIL PROJECT / JANE FURSE
Designed around the people who depend on it
Engagement is required from planning through handover and ongoing operations.
06
BENEFICIARY 01
PATIENTS
Faster access to records; fewer avoidable delays.
BENEFICIARY 02
DOCTORS & NURSES
Less paperwork; more time for direct care.
BENEFICIARY 03
ADMIN & FINANCE
Reliable computing, reporting and connected systems.
BENEFICIARY 04
ICT TEAM
New skills; less reactive repair work.
BENEFICIARY 05
HOSPITAL MANAGEMENT
Better reporting, governance and decisions.
BENEFICIARY 06
MUNICIPALITY
A model for extending district ICT services.
BENEFICIARY 07
SUPPLIERS
More reliable purchase orders and delivery tracking.
BENEFICIARY 08
COMMUNITY
Improved access to dependable rural healthcare.
Engagement methods: requirements workshops • steering committee • staff communication • practical training • community awareness

## Slide 8
WIL PROJECT / JANE FURSE
The proposed solution: one connected environment
Infrastructure, systems and operating practices are planned as a single solution.
07
01
CONNECT
1 km fibre + Openserve
4G/5G failover
02
EQUIP
45 end-user devices
12 network printers
03
CENTRALISE
2 servers + 32 TB NAS
EHR and shared data
04
SECURE
Firewall, VLANs, MFA
Encryption and logs
05
SUSTAIN
Training, SOPs, SLA
Backup & recovery
DESIGN PRINCIPLE
Protect patient-care continuity first; make the system manageable for a three-person ICT team.

## Slide 9
WIL PROJECT / JANE FURSE
Connectivity: fibre first, fail over automatically
Build a dedicated path between the municipality and the hospital.
08
MUNICIPALITY
Existing district network
1 KM FIBRE LINK
12-core OS2 single-mode
Buried route preferred
HOSPITAL EDGE
FortiGate NGFW
SD-WAN monitoring
LAN / USERS
20 wards + 5 offices
BACKUP WAN
Dual-SIM 4G/5G router
Proposed service targets
≥100 Mbps
Project minimum target
200 Mbps
Proposed bearer; scalable to 1 Gbps
≤10 ms
Target latency
99.9%
Uptime target

## Slide 10
WIL PROJECT / JANE FURSE
Physical network architecture
A layered layout connects the external carrier, core equipment, servers and clinical users.
09
OPENserve / MUNICIPALITY
Fibre handoff
FORTIGATE 100F
NGFW • IDS/IPS • SD-WAN
CORE SWITCH
Layer 3 • 10 Gb uplinks
ACCESS SWITCHES
Ward & office cabinets
SERVER RACK
2 servers + 32 TB NAS
WIRELESS APs
15 Wi-Fi 6 access points
ENDPOINTS
PCs • printers • laptops
UPS + generator support critical equipment; locked cabinets and a cooled server room protect the physical layer.

## Slide 11
WIL PROJECT / JANE FURSE
Logical segmentation limits unnecessary access
Separate clinical, administrative, infrastructure and guest traffic.
10
VLAN
SEGMENT
SUBNET
ACCESS INTENT
10
Servers
10.10.10.0/24
AD, EHR database, files, Veeam, WSUS — strict access
20
Clinical workstations
10.10.20.0/24
Ward PCs; clinicians access EHR according to role
30
Admin & finance
10.10.30.0/24
Office and finance systems; no clinical records
40
VoIP / medical devices
Future
Reserved for future services
99
Guest Wi-Fi
192.168.99.0/24
Internet only; isolated from hospital VLANs
CONTROL POINT
Firewall rules determine which services can cross segments; guest devices never reach patient-data systems.

## Slide 12
WIL PROJECT / JANE FURSE
Hardware built for shared hospital use
Standardised end-user equipment and network coverage across wards and offices.
11
40
DESKTOP PCs
16 GB RAM • 512 GB SSD
Windows 11 Pro • TPM 2.0
5
LAPTOPS
For management and roaming
LTE module in proposed spec
12
NETWORK PRINTERS
10 MFPs + 2 high-volume mono
Secure print & cost tracking
15
WIRELESS APs
Wi-Fi 6 across hospital
Cloud-managed controller
Coverage planning also includes one core switch, six distribution switches and access switches across the ward cabinets.

## Slide 13
WIL PROJECT / JANE FURSE
Central servers and resilient storage
Local services support day-to-day clinical work while backup copies enable recovery.
12
01 / PRIMARY
Application & database
Windows Server 2022 • Hyper-V
EHR database, AD/DNS/DHCP and finance apps
02 / BACKUP
Backup & file server
Veeam target, file shares and WSUS
RAID storage with redundant power
03 / SHARED STORAGE
32 TB NAS
RAID 6 usable capacity for departmental shares and medical-imaging staging
RESILIENCE IN THE DESIGN
RAID
Tolerates selected drive failures
REDUNDANCY
Dual power supplies / fans
COOLING
Locked, air-conditioned server room
OFFSITE
Encrypted external HDDs held securely

## Slide 14
WIL PROJECT / JANE FURSE
Software stack: infrastructure meets clinical workflows
The detailed design proposes a manageable, integrated set of platform services.
13
SYSTEM
Windows Server 2022
Windows 11 Pro
IDENTITY
Active Directory
Azure AD Connect
VIRTUALISATION
Hyper-V
2 virtual machines
ENDPOINT
Defender / ESET
BitLocker • patching
BACKUP
Veeam Backup & Replication
30-day retention
NETWORK SECURITY
FortiGate FortiOS 7.4
FortiAnalyzer / VPN
Application layer
Bahmni / OpenMRS EHR
mSCOA / Munsoft finance
Inventory + Intralinks
Microsoft 365 + helpdesk
Specific products and configurations are proposals in the source design and should be confirmed during procurement and solution validation.

## Slide 15
WIL PROJECT / JANE FURSE
Electronic health records at the centre
Replace scattered paper records with searchable, permission-controlled digital records.
14
BAHMNI / OpenMRS EHR
Central clinical record + audit trail
DOCTOR
Full clinical access
NURSE
Ward-level access
ADMIN
Demographics only
PHARMACY
Medication-related access
SEARCH
Name / ID / date
PRIVACY
AES-256 at rest; TLS 1.3 in transit
REPORTING
Daily headcount + monthly DHIS statistics
OFFLINE
Local server continues during fibre outage; sync on restoration

## Slide 16
WIL PROJECT / JANE FURSE
Integration removes duplicate work
Connect clinical activity to finance reporting, stock monitoring and supplier ordering.
15
CLINICAL
EHR / Bahmni
Registration • pharmacy
patient activity
FINANCE
mSCOA / Munsoft
Municipal API / SFTP
Reporting without re-entry
SUPPLY CHAIN
Inventory + Intralinks
Stock levels • purchase orders
supplier performance
AUTOMATION DETAIL
A middleware service is proposed to poll stock levels every 2 hours, create purchase orders via the Intralinks API and track deliveries.
Integration target: reliable data flow between hospital systems and municipal processes, with auditability and clear ownership.

## Slide 17
WIL PROJECT / JANE FURSE
Security is layered, not a single product
Controls protect the edge, devices, identities, data and the physical environment.
16
01
NETWORK EDGE
FortiGate NGFW • default-deny • IDS/IPS • web filtering
02
SEGMENTATION
Separate server, clinical, finance and guest VLANs
03
IDENTITY
Unique accounts • role-based access • MFA for sensitive systems
04
ENDPOINT & DATA
Defender / ESET • BitLocker • encrypted patient data
05
MONITORING
FortiAnalyzer logs • alerts to ICT staff • audit trail
06
PHYSICAL
Locked cabinets • controlled server room • CCTV
POPIA alignment • phishing awareness • access reviews • immediate revocation for departing staff and vendors

## Slide 18
WIL PROJECT / JANE FURSE
Backup and recovery are designed for real failure
The proposed 3-2-1 approach separates copies and tests that data can be restored.
17
COPY 1
LOCAL NAS
Fast local recovery
COPY 2
ENCRYPTED HDD
Weekly off-site rotation
COPY 3
CLOUD STORAGE
Azure Blob, South Africa North
SCHEDULE
Sunday full backup; incremental Monday–Saturday
RETENTION
30 dailies + 12 monthlies on NAS
TARGETS
RTO 4 hours for servers • RPO 24 hours
VERIFICATION
Morning email report + monthly restore drill

## Slide 19
WIL PROJECT / JANE FURSE
Keep essential services available during disruption
Network resilience combines power protection, WAN failover and manual procedures.
18
POWER
10 kVA online UPS
Server-room equipment
30 kVA diesel generator
Auto-transfer switch
CONNECTIVITY
Fibre / Openserve primary
Dual-SIM 4G/5G failover
CLINICAL CONTINUITY
Priority 1: patient information, emergency and communications
Manual intake and prescriptions if outage exceeds 2 hours
Recovery priority order
P1
Critical care
P2
Admin / finance / logistics
P3
General office services

## Slide 20
WIL PROJECT / JANE FURSE
SOPs turn the design into repeatable operations
Standard procedures cover installation, everyday support, data protection and continuity.
19
SOP-001
First-line hardware & network incident management
SOP-002
Patient-file backup and restoration
SOP-003
Third-party and vendor access controls
SOP-004
Municipal link and carrier maintenance
MAINTENANCE RHYTHM
DAILY
Availability, security alerts, backups
WEEKLY
Equipment, capacity, incidents
MONTHLY
Patches, account reviews, restore checks
ANNUALLY
DR test, SOP and architecture review

## Slide 21
WIL PROJECT / JANE FURSE
A clear response path reduces downtime
Incidents are logged, contained, investigated, recovered and verified.
20
01
IDENTIFY
Employee alerts ICT
02
DOCUMENT
Time, reporter, device, impact
03
CONTAIN
Isolate affected accounts / systems
04
INVESTIGATE
Assess scope and root cause
05
RECOVER
Restore service or data
06
VERIFY
Test service and record closure
ESCALATION RULE
When local equipment is confirmed healthy but the carrier link is down, escalate to Openserve and advise hospital management.
Always prioritise patient-care systems and document the incident for monthly ICT reporting.

## Slide 22
WIL PROJECT / JANE FURSE
Governance makes safe behaviour the default
Five policy areas establish expectations for access, continuity, assets, use and capability.
21
01
NETWORK SECURITY
Unique accounts • MFA • encryption • locked rooms
02
BUSINESS CONTINUITY
Failover • UPS • 3-2-1 backups • manual override
03
ASSET MANAGEMENT
Lifecycle records • support SLAs • replacement budget
04
ACCEPTABLE USE
Official hospital use • email standards • monitored supplier access
05
TRAINING & CAPACITY
Technical certifications • annual staff awareness • documented handover
Policy and SOP compliance applies to hospital staff, ICT personnel, suppliers and contractors.

## Slide 23
WIL PROJECT / JANE FURSE
A hybrid support model fits a small ICT team
Internal staff own operations; specialist providers handle carrier and complex services.
22
HOSPITAL ICT TEAM • 3 STAFF
OPENSERVE
Fibre service, carrier faults, SLA
NETWORK SPECIALIST
Router, switch, firewall installation
SECURITY PROVIDER
Monitoring, alerts, threat escalation
MSP / HARDWARE
Helpdesk, endpoint and repair support
CONTRACT CONTROLS
SLAs • response / recovery targets • confidentiality • least privilege • MFA • logging • access revocation • cost review

## Slide 24
WIL PROJECT / JANE FURSE
Build the skills to sustain the system
Hands-on training, manuals and knowledge transfer reduce long-term dependency.
23
CAPABILITY 01
NETWORK
Cabling and fibre awareness; switch / router configuration; VLANs and routing
CAPABILITY 02
SECURITY
Firewall administration; patching; malware response; account and access management
CAPABILITY 03
RECOVERY
Backup monitoring; restore procedures; disaster recovery; incident logging
CAPABILITY 04
SERVICE
Helpdesk ticketing; prioritisation; escalation; end-user communication
HANDOVER PACKAGE
As-built diagrams • IP schemas • digital and paper manuals • restore-drill evidence • asset register

## Slide 25
WIL PROJECT / JANE FURSE
Implementation unfolds in five controlled phases
Design and acceptance gates make progress measurable within the 12-month window.
24
01
INITIATE & SURVEY
M1–2
Charter • requirements • site survey
02
PROCURE & PREPARE
M3–5
Equipment • licences • firewall setup
03
CONNECT & DEPLOY
M6–8
Fibre • network • endpoints • apps
04
TRAIN & VALIDATE
M9–10
ICT training • UAT • restore drill
05
HAND OVER
M11–12
SOPs • final tests • acceptance
Months are aligned to the project schedule; critical procurement and fibre activities should begin early to manage rural-location risks.

## Slide 26
WIL PROJECT / JANE FURSE
The 12-month roadmap and milestone dates
Target sequence from project initiation in September 2026 to handover in August 2027.
25
M1
SEP 26
Initiation
M2
OCT 26
Design
M3
NOV 26
Procurement
M4
DEC 26
Fibre
M5
JAN 27
Network
M6
FEB 27
Deployment
M7
MAR 27
Security
M8
APR 27
Integration
M9
MAY 27
Training
M10
JUN 27
Testing
M11
JUL 27
SOPs
M12
AUG 27
Handover
MILESTONE ID
MILESTONE
TARGET
M-01
Initiation complete
Sep 2026
M-02
Design & architecture approved
Oct 2026
M-03
Procurement complete
Nov 2026
M-04
Fibre installation complete
Dec 2026
M-05
Hardware / network deployment
Feb 2027
M-06
Security infrastructure complete
Mar 2027
M-07
Staff training complete
May 2027
M-08
System testing complete
Jun 2027
M-09
Operational handover
Aug 2027

## Slide 27
WIL PROJECT / JANE FURSE
Risk management focuses on delivery and continuity
Plan mitigations before procurement and installation expose the project to delay.
26
RISK
LIKELIHOOD
IMPACT
MITIGATION
Fibre permits / terrain
High
High
Engage authorities early; backup wireless option
Carrier capacity / SLA
Medium
High
Validate Openserve service and restoration commitments
Budget overrun
Medium
High
Early quotes; 15% contingency; strict scope control
ICT skills gap
High
High
Practical training; manuals; first-year support contract
Cyberattack
High
High
Layered security, updates, monitoring and MFA
Power outages
High
High
UPS + generator; test regularly
Integration / adoption
Medium
High
Early testing; stakeholder workshops and user training

## Slide 28
WIL PROJECT / JANE FURSE
Budget estimate: R8.3 million to R14.5 million
Planning estimate in South African rand; actual costs depend on procurement and validation.
27
R8.3m
LOW ESTIMATE
R14.5m
HIGH ESTIMATE
Network infrastructure
R2.5m–R4.0m
Hardware
R2.3m–R4.0m
Security
R0.6m–R1.2m
Software
R0.5m–R1.0m
Backup power
R0.4m–R0.8m
Training & project management
R0.8m–R1.6m
Contingency (15%)
R1.2m–R1.9m
Budget values are estimates from the project documents. Confirm line-item scope and overlaps during the procurement baseline.

## Slide 29
WIL PROJECT / JANE FURSE
Sustainability is designed into operations
Long-term reliability depends on budgeting, operational discipline and knowledge transfer.
28
OPERATING BUDGET
Annual provision for internet, licences, maintenance and hardware replacement.
VENDOR RELATIONSHIPS
Clear SLA, response and restoration targets, ongoing performance monitoring.
LOCAL CAPABILITY
Three ICT staff trained; manuals and as-built documentation retained.
PREVENTIVE CARE
Daily checks, monthly restore tests, annual DR and architecture review.
ASSET LIFECYCLE
Warranty and support agreements; e-waste handled through municipal policy.
COMMUNITY OWNERSHIP
Awareness and engagement to build confidence in improved services.
SUCCESS MEASURES
≤10 ms latency target • 99.9% uptime target • minimum 40 PCs • automated verified backups • staff training completed

## Slide 30
FROM CONNECTIVITY
TO BETTER CARE.
A secure, integrated and sustainable digital foundation for Jane Furse Memorial Hospital.
THE PROJECT TEAM
Kamohelo Makate
Ally Moremi
Karabo Mosupi
Thabiso Makhubedu
Makhosonke Sibanyoni
Phomello Mokonyane
SOURCE BASIS
WIL Task 1
Project charter, scope, risks, budget and milestones
WIL Task 2
System and application software, hardware, network architecture, SOPs, governance and outsourcing
12-MONTH DELIVERY
Thank you